## Slide 1: Reading Partner GDP PAL Chips
Miha Grčar
2024/25

## Slide 2: PAL 10L8
10 inputs
8 outputs
No feedbacks, no HI-Z states, no registers, no I/O pins…
Output is OR of max two AND expressions
Easy to read
  Read outputs for all combinations of inputs

## Slide 3: PAL 16L8
10 inputs
2 outputs
  Can be set to HI-Z
6 I/O pins
  Implicit feedbacks
  Can be set to HI-Z (become inputs)
Setting HI-Z is max one “AND” expression
Output is “OR” of max 7 “AND” expressions

## Slide 4: Reading PAL 16L8
Create initial set of all possible inputs: 0 .. 210 – 1
For each input…
  Note down the outputs
  Check every I/O pin if it is in HI-Z
  If HI-Z states are found, add additional inputs into the set of all possible inputs
Example
  00_000000_1001101000  11_11110Z
  Adds one new input: 00_000001_1001101000

## Slide 5: PAL 16R4
8 inputs
4 I/O pins
  Implicit feedbacks
  Can be set to HI-Z (become inputs)
4 register outputs
  Explicit feedbacks
  Store value on clock pulse
  Can’t [really] be in HI-Z, but there’s OE
Setting HI-Z on I/O is max one “AND” expression
Output is “OR” of max 7 “AND” expressions

## Slide 6: Reading PAL 16R4
State graph
  State: 4-bit state, register outputs
  Node
    State – 4-bit state (register outputs)
    Mappings – All possible input-to-output mappings (registers are ignored)
    Inputs – Queue of all possible inputs
    Outlinks – Pointers to other states in the state graph

## Slide 7: Reading PAL 16R4
Get_or_create_node(state)
  Create new node (= explore new state)
    Create initial set of all possible inputs: 0 .. 28 – 1
    For each input… (no clock pulse!)
      Note down the outputs (attach these to node.mappings)
      Check every I/O pin if it is in HI-Z
      If HI-Z states are found, add additional inputs into the set of all possible inputs
    Create a queue of all the inputs that were mapped (attach it to node.inputs)
  Get existing node
    Simply fetch the node object corresponding to state
Same as reading 16L8!

## Slide 8: Reading PAL 16R4
Main program
  Set inputs to 0, fire clock pulse, read the initial state (state = register outputs)
  Node = get_or_create_node(initial_state)
  Main loop
    Node.inputs.count() > 0:
      Inputs = node.inputs.dequeue()
      Read outputs with clock pulse *state transition*
      New state = outputs from registers (4 bits)
      Child_node = get_or_create_node(new state)
      Node.outlinks[inputs] = child_node
      Node = child_node (restart main loop)
    Node.inputs.count() == 0:
      Find path to a node that still has some unexplored inputs (restart main loop)
      If no such node is found, we are done

## Slide 9: Toy Example
Mappings:
Inputs I1  Outputs O1
Inputs I2  Outputs O2
Inputs I3  Outputs O3
Node A
Node B
Node C
Inputs I1 + clock
Inputs I2 + clock
Inputs I3 + clock