## Slide 1: Reading Partner GDP PAL Chips
Miha Grčar
2024/25

## Slide 2: PAL 10L8
10 inputs
8 outputs
No feedbacks, no HI-Z states, no registers, no I/O pins…
Output is OR of max two AND expressions
Easy to read
  Read outputs for all combinations of inputs

## Slide 3: PAL 16L8
10 inputs
2 outputs
  Can be set to HI-Z
6 I/O pins
  Implicit feedbacks
  Can be set to HI-Z (become inputs)
Setting HI-Z is max one “AND” expression
Output is “OR” of max 7 “AND” expressions

## Slide 4: PAL 16L8
Reading
  Create initial set of all possible inputs: 0 .. 210 – 1
  For each input…
    Note down the outputs
    Check every I/O pin if it is in HI-Z
    If HI-Z states are found, add additional inputs into the set of all possible inputs
Example
  00_000000_1001101000  11_11110Z
  Adds one new input: 00_000001_1001101000

## Slide 5: PAL 16R4
8 inputs
4 I/O pins
  Implicit feedbacks
  Can be set to HI-Z (become inputs)
4 register outputs
  Explicit feedbacks
  Register value on clock pulse
  Can’t [really] be in HI-Z, but there’s OE
Setting HI-Z on I/O is max one “AND” expression
Output is “OR” of max 7 “AND” expressions

## Slide 6
Outputs O1
Outputs O2
Outputs O3
Inputs I
Inputs I + Clock
Inputs I + Clock
Inputs I
Outputs O1
Outputs O3
Inputs I
Inputs I + Clock
Outputs O4
Inputs I + Clock